Additional file 1a: ACQUISITION.JNL

I: SAVEIMAGE

Run Journal["MOVEZ SUR CEL"]

1.	Device.Focus.CurPos = "Z"+str[ret]

2.	Delay[2,SECONDS]

Run Journal C:\retine\journals\ACQ EXPLAN\MOVEZx40.JNL

3.	Delay[10,MILLISEC]

Run Journal["autofocus2"]			See details on page 2 (II: AUTOFOCUS-2)

Device.Focus.Top = FOCUS+4

Device.Focus.Bottom = FOCUS-4

Device.Focus.Home = FOCUS

Trace [FOCUS]

4.	Legacy:MetaDevice Shutter - Open[]

5.	Overwrite "Z" = Acquire Z Series[BOTTOM, TOP, HOME, USEPLANECOUNT, 9, '''','''']

6.	Shutter - Close[]

7.	Set Image Zoom[[Last Result],50]

8. 	im = "explan"+str[ret]10: Select Image[" "]

9.	surface = Image.ZDistance

10.	Icol = floor[[Region.left+Region.Width]/Region.Width]

11.	ligne = floor[[Region.Top + Region.Height]/ Region.Height]-ligne0+1

12.	ligne = floor([Region.Top + Region.Height]/ Region.Height]

13.	cpt_L = floor((lligne]/26+1

14.	cpt_ii = lligne -floor[lligne/26)*26+1

15.	cpt_L = if[test>1,cpt_L = cpt_L+1, cpt_L]

16.	col = floor[[Region.left]Region.Width]/Region.Width]

17.	ligne = CHR[64+cpt_L]+CHR[96+cpt_II]

18.	col = if[LEN[str[col]]=1,"0"+str[col]]

19.	imname = "scan_"+ligne+str[col]

20.	Select Image[" "]

21.	Define Image Property[[Last Result], "ligne", 0]

22.	Define Image Property[[Last Result], "col", 0]

23.	Define Image Property[[Last Result], "surface", 0]

24.	Image.ZDistance = surface

25.	Image.StageLabel = ligne+str[col]

26.	Image.Wavelength = 0

27.	Image.ZAbsolute = surface

28.	Preferences[]

Run Journal["IMSAVE"]

29.	Run User Program["retine.UserMethods", "IMSAVE", NOKEEPINMEM]

IF boucle=1 THEN

30.	Select Image[" "]

ex =	 Image.FileDrive+image.FileDir+"explan.jpg"

32.	Select Image[" "]

Image.FilePath = ex

33.	Select Region((Last Result], "11111111"]

34.	Save[[Last Result]]

ELSE

END IF

boucle = boucle+1

35.	SelectIMAGE[3 3]

rep = Image.FilePath

36.	Run User Program["retine.UserMethods","exc", NOKEEPINMEM]

37.	Overwrite "Maximum" = Stack Arithmetic["Z"]

38.	Set Image Zoom["Maximum" = Stack Arithmetic["Z"]

39.	Auto Threshold for Dark Objects[]

41.	Overwrite [Source] = Clip Image["Maximum", 0]

42.	Image/Plane with Zoom([Last Result]]

43.	Copy[(Last Result])

44.	im = "explan"+str[ret]

45.	Select Image[" "]

46.	Paste[[Last Result])

47.	Close["Maximum"]

48.	Close["Zoomed Copy of Maximum"]

***End of Journal***

II: AUTOFOCUS-2

1.	"Noshutter" = Acquire - Load Setting[EXPOSURE and BINNING and REGION and ILLUMINATION and DISPLAY and SETTING NAME and SAVING and CORRECTION and CORRIMAGES and ANNOTATION and SPECIAL and COLOR SCALING]

2.	Legacy: MetaDevice Shutter - Open[]

3.	Camera. Digital.Exposure = 20

4.	Auto Expose[]

5.	Close[[Last Result]]

6.	Find Focus[32,6,NOBACKLASH]

7.	Adjust Focus[8, 3.33333, NOBACKLASH]

8.	Shutter - Close[]

9.	"retine NOS" = Acquire - Load Setting[EXPOSURE and BINNING and REGION and ILLUMINATION and DISPLAY and SETTING NAME and SAVING and CORRECTION and CORRIMAGES and ANNOTATION and SPECIAL and COLOR SCALING]

10.	Auto Expose[]

11.	Shutter - Close[]

12.	Delay[25, MILLISEC]

FOCUS = Device.Focus.CurPos

testz = [[[FOCUS<[z0+50] ] and [FOCUS>[Z0-50]]]

WHILE testz=0 DO

FOCUS = Device.Focus.CurPos

13.	Select Image[[10: Auto Expose]]

FOCUS = Image.ZAbsolute

testz = [[[FOCUS<[z0+50] ] and [FOCUS>[Z0-50]]]

IF testz=0 THEN

FOCUS + Z0

testz= 1

ELSE

END IF

WEND

14.	Close [[10:Auto Expose]]

15.	Legacy: MetaDevice Shutter - Open[]

***End of Journal***

Additional file 1b: COUNTING.JNL

I: FINDSPOT\3D Measurements

Max0=0

Stereo=0

name =right[Image.Name.4]

Run Journal["Variables"]

1.	nompile = Image.FileName

2.	Select Image[(Current At Start)]

Z = Image.ZAbsolute

SurfMin = 100

SurfMax = 1000

3.	Open Summary Log[OPENFILE and OVERWRITEMODE, "best focus"]

4.	Pause Summary Logging []

5.	New "Best Focus" = Stack Arithmetic[(Current At Start])

6.	Overwrite [6: Stack Aritmetic] = Basic Filters[[6: Stack Arithmetic],3, 3, 1]

Run Journal C:\retine\3DvolMM6\FindSpots\auto_dark.JNL

7.	Threshold Image[(6: Stack Arithmetic), 1000, 4095, Inclusive]

8.	Integrated Morphometry - Reset Current[]

9.	Integrated Morphometry - Reset Filters[]

10.	Integrated Morphometry - Load State["best focus"]

11.	Integrated Morphometry - Measure[[6:  Stack Arithmetic],-1]

12.	Show Region Statistics [[Last Result], ENTIREIMAGE]

13.	Integrated Morphometry - Log Data[[6: Stack Arithmetic],SUMMARY,CURRENTDATA,1,2]

Fd = ShowRegionStatistics.Minimum

max = IMASummary.Max

max = 0

14.	Integrated Morphometry - Reset Current []

15.	Threshold Image["Best Focus" , 1000, 4095,Inclusive]

16.	Adjust Digital Contrast[[6: Stack Arithmetic],ALL, 50, 50, 1.93

17.	Show Region Statistics[[6: Stack Arithmetic], ENTIREIMAGE]

BI = ShowRegionStatistics.Average

18.	Auto Threshold for Light Objects[Legacy heuristic algorithm]

19.	Show Region Statistics[[6: Stack Arithmetic], ENTIREIMAGE]

Cperc = ShowRegionStatistics.PctThresholdeArea

20.	Threshold Image["Best Focus", 1000, 4095,Inclusive]

21.	Pause Summary Logging[]

22.	Integrated Morphometry - Measure["Best Focus" ,-1]

23.	Integrated Morphometry - Log Data["Best Focus", SUMMARY, CURRENTDATA,1,2]

24.	Resume Summary Logging[]

Dcel = IMASummary.Count

Trace[["B="]str[BI]+ " C="+str[Cperc]+" D="+str[Dcel]]]]

25.	Integrated Morphometry - Clear Object Overlay[[6: Stack Arithmetic)]

IF [BI< B]AND[Cperc<C] THEN

TEST_Filtre = 1

ELSE

IF Dcel>D THEN

TEST_Filtre = 1

ELSE

TEST_Filtre = 0

END IF

END IF

26.	Close Summary Log[]

IF max=0 THEN

27.	Set Image Zoom[[Last Result], 50]

28.	Threshold Image[[Last Result],0,0]

29.	Integrated Morphometry - Reset Current []

30.	Set Image Zoom[[Last Result],100]

31.	New "Overlay Images" = As Displatyed[[Last Result]]

comptage = 0

count = 0

count = 0

comptage = "Excl"

32.	Close[[Current At Start]]

IF [Fd<FondMax] THEN

IF[MAX< AMAS]AND[DARK<DARK8MAX]AND[test8fILTRE+1] then

33.	Threshold Image[[6: Stack Aritmetic], 1000,4095,Off]

34.	Select Image[[Current At Start]]

IF rapide=0 THEN

Run Journal C:\retine\3DvolMM6\FindSpots\spots3D.JNL

35. 		Close[["Close-Open"]

36. 		Close[["Close-Open-2"]

37. 		Close["Maximum-2"]

38. 		Close["Maximum"]

39. 		Close["No Neighbors"]

40. 		Close[[Current At Start]]

ELSE

IF rapide=1 THEN

41. 		Overwrite"FAST" = Stack Arithmetic[[Current At Start]]

Run Journal C:\retine\3DvolMM6\FindSpots\spots3D Rapide.JNL

42. 		Close["Close-Open"]

43. 		Close["Close-Open2"]

44. 		Close["FAST"]

45. 		Close["FAST"]

46.		Close[[Current At Start]]

ELSE

IF rapide=2 THEN

47.		Overwrite "FAST" = Stack Arithmetic[[Current At Start]]

Run Journal C:\retine\3DvolMM6\FindSpots\spots3D Rapide2.JNL

48.		Close["Close-Open"]

49.		Close["Close-Open-2"]

50.		Close["NN"]

51.		Close["FAST"]

52.		Close[[Current At Start]]

ELSE

END IF

END IF

END IF

ELSE

53.		Set Image Zoom[[Last Result],100]

54.		Threshold Image[(Last Result],0,0]

55.		Integrated Morphometry - Reset Current[]

56.		New "Overlay images" = As Displayed[[6: Stack Arithmetic]]

count = 0

comptage = "Excl"

57.		Text[[Last Result],4, 19,0,0,255,MS Sans Serif, Regular,24,"%comptage%  [%count%] %name%dark_max=%dark%"]

58.		Close[[6: Stack arithmetic]]

59.		Close[[Current At Start]]

END IF

ELSE

60.	   Set Image Zoom[[Last Result],50]

61.	   Threshold Image[[Last Result], 0,0]

62.	   Integrated Morphometry - Reset Current[]

63.	   Set Image Zoom[[Last Result], 100]

64.	   New "Overlay Images" = As Displayed[[Last Result]]

65.					comptage = 0

66.					count = 0

count = 0

comptage = "Excl"

67.	   Close'(Current At Start]]

END IF

68.	Define Image Property'[Last Result], "comptage", "%comptage%"]

69.	Define Image Property[[Last Result], "col", "%col%"]

70.	Define Image Property[[Last Result], "ligne", "%ligne%"]

71.	Define Image Property[[Last Result], "Z", "%Z%"]

72.	Image.Annotation = str[comptage]

73.	Image.Wavelength = comptage

74.	Image.IllumSetting = comptage

75.	Text'(Last Result],4400,0,0,255,MS Sans Serif,Regular,24"Fond=%Fd%

76.	Adjust Digital Contrast["Overlay Images",ALL,50,50,1,19]

IF ImageExists["Best Focus"] THEN

77.	Close["Best Focus"]

ELSE

END IF

***End of Journal***

II: Editor\variables (* Value of the variables used in the study)

- B = Best Focus average intensity

B = xxxx (=4000)*

- C = Pourcentage Best Focus Threshold autothreshold area percentage

C = xxx (=100)*

- D = Nombre de cellules détectées sur Best Focus avant traitement

D = n+1

- Spotcutoff = xx (=30)*

- Spotsize = xx (=19)*

- SurfSpot = xx (=30)*

- IntMin = x (=0)*

- NBObjectsMin = n

- FondMax = xxxx (=1250)*

- Cluster = 10x (=108)*

- Dark_max = 10x (=103)*

- Rapide = 0 Mesure 3D Normal

- Rapide = 1 Mesure 3D rapide

- rapide = 1

***End of Journal***